###### SECTION 1: SUBSTANCE/MIXTURE IDENTIFICATION AND MANUFACTURER/SUPPLIER IDENTIFICATION

1.1. Product identification

###### POLYESTER THINNER

1.2. Relevant identified uses of the substance or mixture and uses advised against

For professional use in car refinish.

1.3. Data of the safety data  sheet supplier

Przedsiębiorstwo RANAL Sp. z o.o.

Ul. Warszawska 36a

PL 42-240 Rudniki

Tel: +48 34 329-45-03

Fax: +48 34 320-12-16

Person responsible for the safety data sheet

e-mail: ranal@ranal.pl

1.4. Emergency telephone

+48 34 329-45-03 (from 7:30 am. to 3:30 pm.)

SECTION 2:  HAZARDS IDENTIFICATION

2.1.  Classification of the substance or mixture

Klasyfikacja 1272/2008/EC:

Serious eye damage/irritating to eyes 2 (Eye Irrit. 2) Irritating to eyes. Harmful to reproduction (Repr. 2) Suspected of damaging the unborn child. Toxic to organs – single exposure (cat. 3). Narcosis (STOT SE 3). May cause drowsiness or dizziness. Flammable liquid 2. (Flam. Liq. 2). Highly flammable liquid and vapour.

Classification 1999/45/EC:

The mixture  was classified as dangerous according to current regulations – see section 15.

Harmful product. Irritating to eyes. Harmful to reproduction cat. 3: Possible risk of harm to the unborn child. Harmful: may cause lung damage if swallowed. Highly flammable.

2.2. Label elements:

Contains: Toluene

Signs:

Marking: Danger

Risk index:

H225 Highly flammable liquid and vapour.

H319 Causes serious eye irritation.

H361d Suspected of damaging the unborn child.

H336 May cause drowsiness or dizziness.

.

Safety index:

P210 Keep away from heat/sparks/open flames/hot surfaces – No smoking.

P260 Do not breathe dust/fume/gas/mist/vapours/spray.

P271 Use only outdoors or in a well-ventilated area.

P280 Wear protective gloves/protective clothing/eye protection/face protection.

P312 Call a POISON CENTER or doctor/physician if you feel unwell.

2.3. Other hazards

No data available.

SECTION 3:  COMPOSITION/INFORMATION ON INGREDIENTS

3.1. Substances

Not applicable.

3.2. Mixtures

Product identification

###### POLYESTER THINNER

| Substance name | Identification numbers | Classification and marking | Concentration [%] |
| --- | --- | --- | --- |
| Ethyl acetate | EC: 205-500-4 CAS: 141-78-6 Index no: 607-022-00-5 Registration no: 01-2119475110-46-XXXX | Classification 67/548/EEC: F; R11 Xi; R36 R66-67 Classification 1272/2008/EC: Flam. Liq. 2; H225; Eye Irrit. 2; H 319 STOT SE 3; H336 | 85-95% |
| Toluene | WE: 203-625-9 CAS: 108-88-3 Index no: 601-021-00-3 Registration no: -- | Classification 67/548/EEC: F; R11 Xn; R48/20,R65 Xi; R38, R67 Repr.cat.3 R63 Classification 1272/2008/EC: Flam. Liq. 2 H225 Repr. 2; H361d Asp. Tox. 1 STOT RE 2; H304; H373 Skin Irrit. 2; H315 STOT SE 3; H336 | 5-9% |

Full text of the phrases identifying the types of hazard and R phrases provided in section 16.

SECTION 4: FIRST AID MEASURES

4.1. Description of first aid measures:

General information:

See section 11 of the Material Safety Data Sheet.

Inhalation:

Take the victim outside to the fresh air, ensure quiet surrounding, in case of no breath ensure artificial respiration. Call a doctor.

Skin:

Take off contamined clothing. Rinse contamined skin with plenty of lukewarm water for about 15 min. If irritation persists consult a doctor.

Eyes:

Rinse immediately with plenty of water for about 15 min, avoid strong water jet- risk of comea damage, consult a doctor.

Alimentary tract:

Do not cause vomiting (choking risk). Rinse mouth with water. If conscious, administer 1-2 glasses of warm water. Call a doctor. Person giving first aid should wear medical gloves.

4.2. Most important symptoms both acute and delayed

Vapours may cause drowsiness and dizziness. Repeated exposure may cause skin dryness or cracking.

4.3. Indications of any immediate medical attention and special treatment needed

Special measures allowing for specialist and immediate aid should be available in the place of work.

SECTION 5: FIREFIGHTING MEASURES

5.1. Extinguishing media

Powder, foam resistant to alcohols, carbon dioxide, water mist.

5.2. Special hazards arising from the substance or mixture

Carbon monoxide may be generated in case of  fire.

5.3. Advice for firefighters

Fire-fighting teams should wear self-contained breathing apparatus and light protective clothing. Cool adjacent tanks by spraying water from a safe distance.

SECTION 6: ACCIDENTAL RELEASE MEASURES

6.1. Personal precautions, protective equipment and emergency measures

For persons not being members of aid giving staff:

Remove ignition sources. Ensure sufficient ventilation of the room. Avoid direct contact with the released substance. Avoid contact with skin and eyes. Personal safety measures – see section 8 of Material Safety Data Sheet.

For persons being the members of aid giving staff:

Persons giving aid should wear protective clothing made of coated impregnated fabric, protective gloves (viton), tight protective glasses and breathing apparatus: gas mask with A type absorber.

6.2. Environmental precautions

Prevent leakage to the sewage system, surface waters, underground waters and soil.

6.3. Methods and materials for containment and cleaning up.

Stop the leakage (close the liquid inflow, seal), place damaged container in an emergency container, remove the liquid mechanically and place it in an emergency container. In case of large leakage  embank the area. In case of small amounts, collect with the use of a binding agent (e.g. mica, diatomaceous earth, sand).

6.4. Reference to other sections

Personal protection measures– see section 8 of the Material Safety Data Sheet.

Disposal considerations – see  section 13 of the Material Safety Data Sheet.

SECTION 7: HANDLING AND STORAGE OF SUBSTANCES  AND MIXTURES

7.1. Precautions for safe handling

Keep away from heat and sources of ignition. Prevent leakage to the sewage system, surface waters, underground waters and soil. Use only in well ventilated rooms. Do not smoke. Do not inhale vapours. Avoid contact with skin and eyes. Take precaution measures against electrostatic discharge. Use personal protection measures – see section 8 of the Material Safety Data Sheet.

7.2. Conditions for safe storage including any incompatibilities

Store in well sealed original containers. Do not store near large amounts of organic peroxides or other strong oxidants. Take precaution measures against electrostatic discharge. Store in cool, well ventilated rooms.

Protect from the sunrays, heat sources and low temperatures.

7.3. Special end use(s)

For professional use in car refinish taking into consideration the information included in subsections 7.1 and 7.2.

SECTION 8: EXPOSURE CONTROL/PERSONAL PROTECTION MEASURES

8.1. Control parameters

Ethyl acetate CAS 141-78-6:

- TRGS 900:		MAK: 400ppm, MAK: 1500 mg/m³, 2(I), DFG, Y

- Adopted National Exposure Standards for Atmospheric Contaminants in the Occupational Environment

[NOHSC:1003(1995)]:	TWA 200 ppm –mg/m³, STEL 400ppm, --mg/m³

Toulene CAS 108-88-3 according to:

- TRGS 900:			 MAK:50ppm, MAK:190mg/m³, 4(II), DFG, H, Y

- Adopted National Exposure Standards for Atmospheric Contamonants in the Occupational Environment

[NOHSC:1003(1995)]:		 TWA 50ppm 191 mg/m³, STEL 100ppm, 384 mg/m³, Sk

8.2. Exposure control

Respiratory tract protection:

Gas mask with A type absorber (EN 141).

Hand protection:

Protective gloves PN-EN 374-3 (viton, 0,7 mm thick, penetration time > 480 min, butyl rubber, 0,5 mm thick, penetration time >=480 min)

Eye protection:

Tight protective glasses.

Skin protection:

Proper protective clothing (coated, impregnated fabrics).

Workplace:

Fixed fume extraction and general ventilation.

Environmental exposure control:

Prevent leakage to the sewage system, surface waters, underground waters and soil.

SECTION 9: PHYSICAL AND CHEMICAL PROPERTIES

9.1. Information on basic physical and chemical properties

| Parameter | Value |
| --- | --- |
| Physical state | liquid |
| Colour | clear |
| Odour | strong, powerful |
| Odour treshold | 0.18-670 mg/m3 (ethyl acetate) |
| pH | not applicable |
| Melting / freezing point | -83°C |
| Boiling point | 77-110°C |
| Flash point | about 2°C |
| Autoignition point | 460°C |
| Breakdown point | not specified |
| Evaporation rate | not specified |
| Flammability (solid, gas) | not applicable |
| Explosion limits | % bottom: 1.2 vol% top: 7 vol% (toluene) |
| Vapour pressure | 98 hPa (20°C) (ethyl acetate) |
| Vapour density(with regard to air) | 3.04 (ethyl acetate) |
| Density | about 0.89 g/cm3 (20°C) |
| Solubility (in water) | very poor |
| n-oktanol/water division ratio | 0.66 (ethyl acetate) |
| Viscosity | about 1mPas |
| Explosive properties | not applicable |
| Oxidizing properties | not applicable |

9.2. Other information

No data available

SECTION 10: STABILITY AND REACTIVITY

10.1. Reactivity

Product not reactive under normal conditions.

10.2. Chemical stability

Product stabile under normal conditions.

10.3. Possibility of hazardous reactions

Carbon monoxide and other toxic gases are generated in case of fire.

10.4. Incompatible materials

Highly flammable. Avoid contact with large amounts of organic peroxides, strong acids and bases, as well as other strong oxidants. Take precaution measures against electrostatic discharge. Protect from the sunrays, heat sources and low temperatures.

10.5. Incompatible materials

Avoid contact with large amounts of organic peroxides, strong acids and bases, as well as other strong oxidants

10.6. Hazardous decomposition products

Carbon monoxide and other toxic gases are generated as a result of thermal decomposition.

SECTION 11: TOXICOLOGICAL INFORMATION

11.1. Information on toxicological effects

No experimental data available on the preparation. Evaluation based on the data on dangerous ingredients included in the preparation.

a) Acute toxicity

Ethyl acetate

LD50 (rat, ingestion) – 5620  mg/kg

LC50 (rat, inhalation) – 200 gm/m3

Toluene

LD50 (rat, ingestion) – 5000  mg/kg

LC50 (rat, inhalation) – 15320  mg/m3 /4h

b) Irritating effect

Skin: irritating to skin and mucous membrane

Eyes: irritating effect

c) Caustic effect

Mixture is not classified as caustic. No available data confirming the hazard class.

d) Allergic effects

Mixture is not classified as having allergic effects. No available data confirming the hazard class.

e) Toxicity for repeated exposure

Repeated exposure may cause skin dryness or cracking.

f) Cancerogenity

Mixture is not classified as carcinogenic. No available data confirming the hazard class.

g) Mutagenity

Mixture is not classified as mutagenic. No available data confirming the hazard class.

h) Harmful effect on reproduction

Possible risk of harm to the unborn child.

Exposure methods:

Respiratory tract: Harmful in case of inhalation.

Skin: Irritating to skin.

Eyes: Irritating to eyes.

If swallowed the substance may cause irritation of the alimentary tract, nausea, vomiting and diarrhea. Harmful; if swallowed the substance may cause lung damage.

Poisoning symptoms:

Headaches and dizziness, fatigue, decreased muscle power, drowsiness and in exceptional instances loss of consciousness. Vapours may cause drowsiness and dizziness. Repeated exposure may cause skin dryness or cracking.

SECTION 12: ECOLOGICAL  INFORMATION

No experimental data available on the preparation. Evaluation based on the data on dangerous ingredients included in the preparation.

12.1. Toxicity

Ethyl acetate

Daphnia magna /NOEC (48 hours) 12 mg/l/21d

Number in catalogue of water hazardous substances:	95

Water hazard class:	1

Toluene

Daphnia magna /EC50 (48 hours) 11 mg/l

Acute toxicity for fish LC50 13mg/l/96 hours

Number in catalogue of water hazardous substances:	194

Water hazard class:	2

12.2. Persistence and degradability

Ethyl acetate

Biodegradability: 100% (THOD)

12.3. Bioaccumulative potential

No data available.

12.4. Mobility in soil

Very poorly soluble in water.

12.5. Results of PBT and vPvB assesment

No data available.

12.6. Other hazardous effects

No data available.

SECTION 13: DISPOSAL CONSIDERATIONS

13.1. Waste treatment methods

Product must be disposed of in compliance with the proper local and statutory regulations  with regard to waste – see point 15.

Product remains:

Waste code 07 01 04* Do not dispose the product into the sewage system. Do not store with communal waste.  Remove carefully the remains of the product and leave to dry completely. (only in well ventilated rooms).

CAUTION: The remains should be left to dry only in well ventilated rooms and away from flammable products.

Contamined container:

A contamined container containing unhardened remains of the product is harmful waste. Waste code: 15 01 10*. Do not store with communal waste. The contamined container should be disposed with entities which are authorized to collection, recover o disposal.

SECTION 14: TRANSPORT INFORMATION

14.1.UN number

1263

14.2. UN proper shipping name

PAINT-RELATED MATERIAL

14.3. Transport hazard class (es)

3

14.4. Packaging group

II

14.5. Environmental hazards

no

14.6. Special precautions for user

Do not transport together with products of class 1 (except products of class 1.4S), and some products of class  4.1 and 5.2. During the transport avoid direct contact with products of class 5.1 and 5.2. Do not use an open flame and do not smoke.

14.7. Transport in bulk according to Annex II of MARPOL 73/78 Convention and the IBC Code

Not applicable.

SECTION 15: REGULATORY INFORMATION

15.1. Safety, health and environmental regulations / legislations specific for the substance or mixture

- Directive 67/548 /EWG (2006/121/WE)

- Directive 91/155/EWG (2001/58/WE)

- Directive 1999/45/EC (2006/8/WE)

- REACH – Regulation 2006/1907/WE

- CLP – Regulation 1272/2008/WE

15.2. Chemical safety assessment

Not performed.

SECTION 16: OTHER INFORMATION

16.1. Full text of the phrases identifying the types of hazards and R phrases mentioned in sections 2-15:

R10 Flammable.

R11 Highly flammable.

R20/21 Harmful by inhalation and in contact with skin.

R48/20 Harmful: danger of serious damage to health by prolonged exposure through inhalation.

R38 Irritating to skin.

R63 Possible risk of harm to the unborn child.

R65 Harmful: may cause lung damage if swallowed.

R66 Repeated exposure may cause skin dryness or cracking.

R67 Vapours may cause drowsiness and dizziness.

Flam.Liq.2

Flam.Liq.3

H225  Highly flammable liquid and vapour.

H226 Flammable liquid and vapour.

Asp. Tox. 1

STOT RE 2 Toxic effect on target organs – repeated exposure (cat.2).

H304 May be fatal if swallowed and enters airways.

H373 May cause damage to organs through prolonged or repeated exposure.

Repr. 2

H361d Suspected of damaging fertility or the unborn child.

STOT SE 3 Toxic effect on target organs – single exposure cat. 3

H336 May cause drowsiness or dizziness

Acute Tox. 4

H332 Harmful if inhaled.

H312 Harmful in contact with skin.

Eye Irrit. 2;

H319 Causes serious eye irritation.

Skin Irrit. 2

H315 Causes skin irritation (category 2)

EUH066 Repeated exposure may cause skin dryness or cracking.

16.2. Explanations of the abbreviations  and acronyms used in the Material Safety Data Sheet:

Nr CAS – numerical symbol ascribed to a chemical substance by the American organization Chemical Abstracts Service (CAS).

Nr EC – a number ascribed to a chemical substance in the European List of Notified Chemical Substances (ELINCS), or a number in the European Inventory of Existing Chemical Substances mentioned in  "No-longer polymers" publication (EINECS)

MPC – maximum permissible concentration of health hazardous substances in the work place.

MPIC – maximum permissible instantaneous concentration.

MPCC – maximum permissible ceiling concentration.

PCB – permissible concentration in biological material

UN number – four-digit identification number of a substance, preparation or product pursuant to UN model regulations

Information based on our current knowledge. This document shall not constitute warranty for product characteristics.

Classification of the mixture is based on classification rules contained in directive 1999/45/EC.

Changes: general update